NOTIFICATION

The following notification is being circulated in accordance with Article 10.6

| 1. | Notifying Member: AUSTRALIA If applicable, name of local government involved (Article 3.2 and 7.2): |
| --- | --- |
| 2. | Agency responsible: Australian Competition and Consumer Commission (ACCC) Name and address (including telephone and fax numbers, email and website addresses, if available) of agency or authority designated to handle comments regarding the notification shall be indicated if different from above: Department of Foreign Affairs and Trade Email: tbt.enquiry@dfat.gov.au |
| 3. | Notified under Article 2.9.2 [X], 2.10.1 [ ], 5.6.2 [ ], 5.7.1 [ ], other: |
| 4. | Products covered (HS or CCCN where applicable, otherwise national tariff heading. ICS numbers may be provided in addition, where applicable): Miniature motorbikes (also known as 'mini bikes' or 'pocket bikes') – a vehicle which resembles a motorcycle but scaled down to about half the size, that is designed to be used by a single person, has a seat height no greater than 600 millimetres and has major dimensions which are scaled down in proportion to the seat height.; - Other (HS 871190). |
| 5. | Title, number of pages and language(s) of the notified document: Consumer Goods (Miniature Motorbikes) Safety Standard 2019 (12 page(s), in English). |
| 6. | Description of content: A regulation banning miniature motorbikes with unsafe design features was introduced in Australia in 2011 (Consumer Protection Notice No 24 of 2011). This has now been replaced with the Consumer Goods (Miniature Motorbikes) Safety Standard 2019. The safety standard maintains the requirements of the Consumer Protection Notice for the design, performance and construction of miniature motorbikes, provides additional clarity with a new definition of a 'miniature motorbike' consistent with the Motor Vehicle Standards Act 1989 (Cth) and introduces new requirements including a speed limiting device, warnings and user instructions. |
| 7. | Objective and rationale, including the nature of urgent problems where applicable: The objective of the Consumer Goods (Miniature Motorbikes) Safety Standard 2019 is to reduce the number of fatalities and injuries associated with the use of miniature motorbikes in Australia. In particular to minimise incidents caused by poorly manufactured miniature motorbikes and those not supplied with basic safety features such as effective brakes, steering, foot pegs and engine cut-out devices. It also improves the safety information provided to consumers.; Consumer information, labelling; Protection of human health or safety; Reducing trade barriers and facilitating trade. |
| 8. | Relevant documents:  Instrument - https://www.legislation.gov.au/Details/F2019L01633  Explanatory statement - https://www.legislation.gov.au/Details/F2019L01633/Explanatory%20Statement/Text  Product Safety Australia page - https://www.productsafety.gov.au/standards/miniature-motorbikes |
| 9. | Proposed date of adoption: The safety standard took effect on 18 December 2019. Proposed date of entry into force: The safety standard provides a 12 month transitional period to allow suppliers to move to the new requirements. During the transitional period suppliers may choose to comply with the new safety standard or the requirements set out in the Consumer Protection Notice No 24 of 2011. |
| 10. | Final date for comments: 60 days from notification; (20 June 2020) |
| 11. | Texts available from: National enquiry point [X] or address, telephone and fax numbers and email and website addresses, if available, of other body: Instrument - https://www.legislation.gov.au/Details/F2019L01633 Explanatory statement - https://www.legislation.gov.au/Details/F2019L01633/Explanatory%20Statement/Text Product Safety Australia page - https://www.productsafety.gov.au/standards/miniature-motorbikes Department of Foreign Affairs and Trade Email: tbt.enquiry@dfat.gov.au https://www.legislation.gov.au/Details/F2019L01633 https://www.legislation.gov.au/Details/F2019L01633/Explanatory%20Statement/Text https://www.productsafety.gov.au/standards/miniature-motorbikes |